## Slide 1
32 BIT RISC PROCESSOR
Athul P – 16116012
Kaustubh Nayyar – 16116030
Khyati Kiyawat – 16111018
Shubhanshu Agarwal – 16118078
Sidharth Thomas – 16112087
Varun Rathore - 16116074
Under the guidance of Prof. Vaskar Raychoudhary

## Slide 2
WHY RISC ?
Simple addressing modes
Simple instruction formats
Focuses on Software
Requires less Hardware
Fixed Size Instructions
Register-to-Register Operations
Single-Clock

## Slide 3
Based on MIPS ISA with few modifications
Dual-Issue Superscalar design
With integrated assembler
“ISA is what lives for years while implementation may change”
INSTRUCTION SET ARCHITECTURE

## Slide 4
R-Type :
Field Positions | 0pcode | rs | rt | rd | shamt | EXTRA BITS
Bit Positions | 31:26 | 25:21 | 20:16 | 15:11 | 10:6 | 5:0
Field Positions | Opcode | rs | rt | Address
Bit Positions | 31:26 | 25:21 | 20:16 | 15:0
I-Type :
Field Positions | Opcode | Address
Bit Positions | 31:26 | 25:0
J-Type :
INSTRUCTION FORMAT

## Slide 5
INSTRUCTIONS
R-Type Instructions :
add
sub
and
or
xor
slt
J-Type Instructions :
jump

## Slide 6
INSTRUCTIONS (con’d)
I-Type Instructions :
addi
andi
lw
sw
ori
xori
slti
bne
beq

## Slide 7
SCALAR DATAPATH
Fig : RTL Schematics of a single 32-bit processor

## Slide 8
SUPER SCALAR DATAPATH
LIMITATIONS
  Limited amount of Instruction-Level Parallelism
  More hardware, more cost
  Limited by dependencies and resource conflicts
WHY SUPERSCALAR ?
  Parallelism improves performance
  Higher throughput
  Faster than scalar rated at same clock frequency

## Slide 9
SUPER SCALAR DATAPATH
Fig : RTL Schematics of a 32-bit Dual-Issue Super Scalar Processor

## Slide 10
SUPER SCALAR DATAPATH (contd.)
Fig : TestBench Waveform of a 32-bit Dual-Issue Super Scalar Processor

## Slide 11
SUPER SCALAR DATAPATH (contd.)
Fig : TestBench Waveform of a 32-bit Dual-Issue Super Scalar Processor (without dependecies)

## Slide 12
ASSEMBLER
INSTRUCTIONS FORMATS :
R format – func $r1 $r2 $r3
lw/sw – lw/sw $r1 $r2 memory_value
I format – func $r1 $r2 constant_value
J format – j address_value
NEED FOR AN ASSEMBLER :
Original design based on pre-loaded instructions in Instruction Memory
Having a High-Level Language input was not an option in Verilog
Assembler provides a platform for High-Level Language input

## Slide 13
ASSEMBLER (contd.)
Fig : Testing the assembler in C++

## Slide 14
INSPECTION MODULE
Inspects the contents of any data location (registers or data memory) at a point of time
Stores this data in a text file in an ordered format
Fig : Running the inspection module in C++

## Slide 15
SCOPE FOR FURTHER WORK
Introducing Pipelining into the current module
Including Out-of-Order issues and execution
Increasing the number of instructions
Implementing flexibility of instruction format based on GPR requirement
FPGA implementation of the processor

## Slide 16
Computer Organization and Architecture, 8th edition-William Stallings
Computer Organization and Design, 4th edition- D.A. Patterson, J.L. Hennessey
Digital Design and Computer Architecture- D.M. Harris, S.L. Harris
Computation Structures- MIT Course EECS 6.004
A Report on 16- bit RISC Processor by R.K.S. Parihar, S.Reddy (BITS Pilani)
www.ocf.Berkeley.edu
www.eg.buknell.edu
REFERENCES